| 091-10-12 | Auto Charge 20 |
| --- | --- |

BATTERY CHARGER

A Kussmaul Auto Charge 20 Series Model #091-10-12, 20 amp multiple battery charger shall be installed.    The charger shall include a front panel mounted amp meter that indicates total output current and protective panel with strain relief connections.

The charger shall have the following operational specifications:

a)  120 volts AC input at 4.7 amps

b)  12 volts DC output at 20 amps

c)   Dimensions of:  12.75” high x 6.75” wide x 4.25” deep and weighs 22 lbs.

The battery charger shall supply a ‘multiple three battery banks’ utilizing independent sense circuits that control voltage and current to each battery, so that parasitic loads on one battery have no effect on the second battery bank.    The unit shall be enclosed in an aluminum enclosure.   The system shall have a built-in sense circuit to check battery voltage 120 times a second.

Full amperage output shall be available to either battery if the adjacent bank does not require charging, optimizing use of available power then charging banks with differing parasitic loads.  The unit shall include front panel connections for a remote display.