| 091-159-430-250 | Super 30 Auto Eject, 4 Pin, 30A, 240V |
| --- | --- |

EJECTION UNIT

A Kussmaul Super 30 Auto Eject Model #091-159-430-250, 4-pin 30 amp 240 volt pin and sleeve contact shore power assembly, cover, solenoid input wire, power cord and plug shall be installed.   The 12 volt unit shall eject the shore power cord away from vehicle path upon sensing engine start; after ejection, the weatherproof cover snaps into position over inlet.  The unit shall have a waterproof sculpted cover with no sharp edges and back enclosure with watertight cable fittings, which protect mechanism from road contamination.   The unit shall sequence energizing of the Auto Eject, eliminating terminal arching when connecting and disconnecting power cord.

A pre-wired 3 foot AC electrical cord and eject sense wire (side wired) shall be installed.   The assembly shall have the following dimensions: 8.9” high x 6.68” wide x 6.2” deep with 8 lb. weight.   Color of cover shall be:  (yellow) (red) (blue) (white) (gray) (black)