| 091-165-24-DV | Auto Charge 12 DV, 24V |
| --- | --- |

BATTERY CHARGER

A Kussmaul Auto Charge #12 Series Model #091-165-24-DV, 6 amp dual voltage battery charger shall be installed.   The charger shall include a front panel amp meter to indicate output and protective front panel and strain relief.

The charger shall have the following operational specifications:

a)  Dual voltage:  120 volts AC input at 2.5 amps or 240 volts AC input at 1.3 amps

b)  24 volts DC output at 6 amps

c)  Dimensions of:  11” high x 5.5” wide x 4.5” deep and weighs 12 lbs.

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure.   The unit shall include front panel connections for an optional remote display.