| 091-170-12 | Auto Charge 12 HO, 12V |
| --- | --- |

BATTERY CHARGER

A Kussmaul Auto Charge #12 Series Model #091-170-12, 20 amp high output battery charger shall be installed.   The charger shall include a front panel amp meter to indicate output and protective front panel and strain relief.

The charger shall have the following operational specifications:

a)  120 volts AC input at 4.7 amps

b)  12 volts DC output at 20 amps

c)  Dimensions of:  12.75” high x 6.75” wide x 4.25” deep and weighs 16 lbs.

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure.   The system shall have a built-in sense circuit to check battery voltage 120 times a second; the system shall compensate for voltage drop in charging wires and provide quick recharging with no overcharging.  The unit shall include front panel connections for a remote display.