| 091-187-12-194 | Auto Charge 1200, w/Status Center |
| --- | --- |

BATTERY CHARGER

A Kussmaul Auto Charge #1200 Series Model #091-187-12-194, 40 amp high output battery charger shall be installed.  The charger shall include a built-in Model #091-194-IND digital display.  The unit shall provide LED digital voltage and amperage readout.  The right side of the display shall have a five segment bar graph indicating output current.  The left side of the display shall have four (4) LED color coded lights shall indicate battery condition.

The charger shall have the following operational specifications:

a)  120 volts AC input at 10 amps

b)  12 volts DC output at 40 amps

c)  Dimensions of:  13.25” high x 7” wide x 5.25” deep and weighs 26 lbs.

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure.   The system shall automatically charge and shall support parasitic DC loads.  The system shall have a built-in sense circuit to check battery voltage 120 times a second; the system shall compensate for voltage drop in charging wires and provide quick recharging with no overcharging.