| 091-18WP-012 | WP Auto Eject (12Vdc/240Vac), 15A |
| --- | --- |

EJECTION UNIT

A Kussmaul WP Series Auto Eject Model #091-18WP-012, 15 amp 12Vdc/240Vac volt shore power assembly, cover, and plug shall be installed.   The 12 volt solenoid shall eject the shore power cord away from vehicle path upon sensing engine start; after ejection, the weatherproof cover snaps into position over inlet.   The assembly shall have the following dimensions:  5.7” high x 3.30” wide x 3.4” deep with 2 lb. weight.   Color of cover shall be:  (yellow) (red) (blue) (white) (gray) (black)