| 091-200-12-194-WT-XX | LPC 40, w/Watertight Display |
| --- | --- |

BATTERY CHARGER AND WATERTIGHT DIGITAL DISPLAY

A Kussmaul Auto Charge LPC 40 Series Model #091-200-12-194-WT-XX Low Profile 40 amp high output battery charger shall be installed and shall include a waterproof Model #091-194-IND-WT-XX digital Status Center.   The unit shall provide LED digital voltage and amperage readout.   The right side of the display shall have a five segment bar graph indicating output current.  The left side of the display shall have four (4) LED color coded lights shall indicate battery condition.  The color of the housing shall be:   (yellow) (white) (red) (gray) (blue) (black)

The charger shall have the following operational specifications:

a)  120/240 volts AC input at 7 amps

b)  12 volts DC output at 40 amps

c)  Dimensions of:  3.3” high x 6.8” wide x 13.25” deep and weighs 7 lbs.

The lightweight and low profile battery charger shall supply a ‘single battery system’ and with an aluminum enclosure.   The unit shall include an auxiliary 15 amp output circuit with power source selector for operating accessory loads.   The unit shall include front panel connections for a remote display.   Charger output shall pose no interference with other electronic systems on the vehicle.