| 091-200-12-IND | LPC 40, w/Bar Graph Display |
| --- | --- |

BATTERY CHARGER AND BAR GRAPH DISPLAY

A Kussmaul Auto Charge LPC 40 Series Model #091-200-12-IND Low Profile 40 amp battery charger shall be installed.   The charger shall include a Model #091-200-IND remote bar graph display.

The charger shall have the following operational specifications:

a)  120/240 volts AC input at 7 amps

b)  12 volts DC output at 40 amps

c)  Dimensions of:  3.3” high x 6.8” wide x 13.25” deep and weighs 7 lbs.

The lightweight and low profile battery charger shall supply a ‘single battery system’ and with an aluminum enclosure.   The unit shall include an auxiliary 15 amp output circuit with power source selector for operating accessory loads.   The unit shall include front panel connections for a remote display.   Charger output shall pose no interference with other electronic systems on the vehicle.