| 091-215-12-194B | Auto Charge 1000 PLC, w/Status Center Display |
| --- | --- |

BATTERY CHARGER, BUILT-IN BATTERY SAVER AND DISPLAY

A Kussmaul Auto Charge #1000 Series Model #091-215-12-194B, 15 amp battery charger and 3 amp Battery Saver and shall include a Model #091-194B-IND digital Auto Charge Status Center.   The unit shall provide LED digital voltage and amperage readout.  The right side of the display shall have a five segment bar graph indicating output current.  The left side of the display shall have four (4) LED color coded lights shall indicate battery condition.

The Auto Charge 1000 with Parasitic Load Compensation (PLC) is a compact, microprocessor controlled, completely automatic, single channel battery charger designed for vehicles with a single battery system. The PLC charger is designed to withstand the shock and vibration encountered by vehicle mounted equipment.

The Battery Saver component shall eliminate drain on vehicle’s battery system when vehicle is not in use.  The system shall automatically disconnect auxiliary vehicle loads from battery when the charger is energized.

Parasitic Load Compensation feature is designed especially to meet the heavy duty requirements of emergency vehicles. Parasitic load compensation allows you to input the total number of parasitic load amps on the vehicle. Then the charger will shift the absorption stage set point so the battery voltage will drop to the float voltage when the desired current is reached. This will lead to a longer battery life and no overcharging or overheating.

The charger shall have the following operational specifications:

- 120 volts AC input at 3.5 amps

- Battery Charger: 12 volts DC output at 15 amps

- Battery Saver: 3 amps 12 volt DC output

- 8 Pin Selector Switch on front panel

  - Battery Type: Lead-Acid, Gel Cell, AGM or Odyssey

  - Float / 3-Step

  - Battery Saver ON/OFF

  - Parasitic Load Compensation

- AC power applied light on front panel

- System LED Status Indicator on front panel

- Dimensions of:  9.35” high x 5.9” wide x 4.725” deep and weighs 11 lbs.