| 091-28HP-24 | Air Eject, High Pressure, 24 volt |
| --- | --- |

AIR EJECTION UNIT

A Kussmaul Air Auto Eject Model #091-28-24 high pressure air hose eject assembly, matting connector, and check valve, with cover shall be installed.   The 24 volt 175 PSI unit shall eject the air hose away from vehicle path upon sensing engine start. The vehicle side mounted pneumatic connector shall be suitable for standard air hose adapters to maintain air pressure on the vehicle’s air brake system in the unit is parked in a building.   (A minimum of 20 PSI shall be required for ejection operation.)

The assembly shall have the following dimensions: 3.6” high x 2.85” deep with 2 lb. weight.