| 091-55-15-120T | Super 15 Trailer Eject, 15A, 120V |
| --- | --- |

TRAILER EJECTION UNIT

A Kussmaul Super Trailer Auto Eject Model #091-55-15-120T, 15 amp 120 volt shore power assembly, cover, solenoid input wire, power cord, and plug shall be installed.   Plug eject mechanism shall be wired to the foot brake pedal, ejecting the plug prior to the vehicle being put in gear.   The 12 volt solenoid shall eject the shore power cord away from vehicle path; after ejection the weatherproof cover shall snap into position over inlet.  The unit shall sequence energizing of an Auto Eject, eliminating terminal arching when connecting and disconnecting power cord.

The unit shall have a waterproof back enclosure with watertight cable fittings, which protect mechanism from road contamination.  A pre-wired 3 foot AC electrical cord and starting sense wire (side wired) shall be installed.

The assembly shall have the following dimensions: 6.17” high x 4.08” wide x 2.8” deep with 4 lb. weight.   Color of cover shall be:  (yellow) (red) (blue) (white) (gray) (black)