| 091-7-12 | Maintenance Master |
| --- | --- |

BATTERY CHARGER

A Kussmaul Maintenance Master Model #091-7-12, 5 amp battery charger shall be installed.  The unit shall be designed specifically for charging auxiliary generator batteries.   The unit shall be equipped with an integral amp meter to indicate charge rate.

The charger shall have the following operational specifications:

a)  120 volts AC input at 1 amp

b)  12 volts DC output at 5 amps

c)   Dimensions of:  9.75” high x 5.50” wide x 5.30” deep and weighs 9 lbs.

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure. The unit shall automatically charge generator batteries and shut-off at charge completion, with no overcharging.