| 091-9-12V-1200 | Pump Plus 1200 System, w/ Bar Graph Display |
| --- | --- |

AIR COMPRESSOR, BATTERY CHARGER, DISPLAY – 1200 PUMP PLUS

A Kussmaul air compressor and battery charger package Model #091-9-12V-1200 shall be installed.    The Auto Pump 12 volt driven air compressor shall ensure that the air brake system is properly pressurized for immediate response of the unit.   A pressure switch shall regulate operation and shall automatically sense low air pressure in the brake system and restore the proper pressure.   The unit shall have no interference with the vehicle mounted air compressor. The compact compressor shall have sealed bearings and a 15 amp circuit breaker installed in pressure switch assembly.  The air compressor power mode selector switch shall select:  1)  DC power full time from vehicle battery  2)  AC powered only from the battery when vehicle is plugged into shore power and automatically shuts off air compressor when disconnected from shore power.

The air compressor shall have the following ratings:

1)  100 PSI maximum rating

2)  Pre-set at 75 PSI “ON” and 95 PSI “OFF”

3)  Adjustable differential range of 20 PSI to 100 PSI

4)  Output:

0.30 SCFM @ 80 PSI

0.35 SCFM @ 60 PSI

5)  Rating: 12 volt at 11 amps

The battery charger shall be a Pump Plus #1200 Series 40 amp high output battery charger shall be installed.     The charger shall include a Model #091-199-001 exterior bar graph display.

The charger shall have the following operational specifications:

a)  120 volts AC input at 10 amps

b)  12 volts DC output at 40 amps

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure.   The system shall have a built-in sense circuit to check battery voltage 120 times a second; the system shall compensate for voltage drop in charging wires and provide quick recharging with no over-charging.  The unit shall include front panel connections for a remote display and auxiliary loads.