| 091-187-12-IND | Auto Charge 1200 Remote w/Bar Graph |
| --- | --- |

BATTERY CHARGER AND BAR GRAPH DISPLAY

A Kussmaul Auto-charge #1200 Series Model #091-187-12-IND, 40 amp high output battery charger shall be installed.     The charger shall include a Model #091-199-001 exterior bar graph display.

The charger shall have the following operational specifications:

a)  120 volts AC input at 10 amps

b)  12 volts DC output at 40 amps

c)  Dimensions of:  13.25” high x 7” wide x 5.25” deep and weighs 26 lbs.

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure.   The system shall have a built-in sense circuit to check battery voltage 120 times a second; the system shall compensate for voltage drop in charging wires and provide quick recharging with no overcharging.  The unit shall include front panel connections for a remote display.