| 091-187-12-R-194 | Auto Charge 1200 Remote, w/Status Center |
| --- | --- |

BATTERY CHARGER AND DIGITAL DISPLAY

A Kussmaul Auto Charge #1200 Series Model #091-187-12-R-194, 40 amp battery charger shall be installed and shall include a Model #091-194-IND digital Status Center. The unit shall provide LED digital voltage and amperage readout.   The right side of the display shall have a five segment bar graph indicating output current.  The left side of the display shall have four (4) LED color coded lights shall indicate battery condition.

The charger shall have the following operational specifications:

a)  120 volts AC input at 10 amps

b)  12 volts DC output at 40 amps

c)  Dimensions of:  13.25” high x 7” wide x 5.25” deep and weighs 26 lbs.

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure.   The system shall have a built-in sense circuit to check battery voltage 120 times a second; the system shall compensate for voltage drop in charging wires and provide quick recharging with no overcharging.  The unit shall include front panel connections for a remote display.