| 440-4910-0 | WP-35, Waterproof Charger |
| --- | --- |

BATTERY CHARGER

A Kussmaul WP-35 Series Model #440-4910-0, waterproof 35 amp battery charger shall be installed.    A remote single bar graph display Model #023-5353-1 shall be installed.

The charger shall have the following operational specifications:

a)  120 volts AC input at 10 amps

b)  12 volts DC output at 35 amps

c)  Dimensions of:  14” high x 6.875” wide x 5.75” deep and weighs 30 lbs.

The battery charger shall supply a ‘single battery system”.   The battery enclosure shall have a sealed case for waterproof operations, with no exterior terminal connections.   The aluminum enclosure shall have integral heat sinks.